## Slide 1
מס' פרויקט:
20-1-1-2187
שם הפרויקט: מימוש וסימולציה של מאיץ למערכות לומדות על רכיב FPGA
מגישים: שי צבר 208723627 חיים גרודה 312562721 מנחה:
יוני זייפרט
מקום ביצוע:
אוניברסיטה

## Slide 2
CNN – Convolutional Neural Network
  Achieved great success in image classification, speech recognition and more.
  Research hotspot in many scientific fields.
  Widely used in the industry, such as for autonomous cars, security systems, health and more.
  CNN Structure
  Convolution - Feature extraction using filters (85-90%)
  Activation – Introduce nonlinearity
  Pooling - Reduce spatial dimensions
  Fully Connected - Final classification decision
Figure: Implemented CNN model
Figure: The “view” of a Tesla autonomous driving computer

## Slide 3
CNN Acceleration
  Motivation
  high accuracy comes with high computation time and high-power consumption
  need to include such image recognition capabilities in embedded systems with tight real-time and power constraints
  Objectives
  Acceleration – by hardware parallelization
  Accuracy – reduce loss due to fixed point arithmetic
  Power – dedicated hardware processing elements
  Utilization – FPGA resources
    Computationally intensive, 85%-90% of computations [source]
Figure: 2D convolution. [source]

## Slide 4
Method
  Fixed Point Calculations:
  Better computation time
  Less hardware resources
  Possible loss of accuracy
  Simulation:
  SW implementation of CNN
  Comparison time HW vs SW
  Compare accuracy HW vs SW
  Evaluate power consumption
  High Level Synthesis (HLS)
  RTL abstraction
  Efficiently build and verify hardware
  Control design optimization

## Slide 5
  Processing system (PS):
  CPU – Input, output, control and configuration
  DDR – memory unit
  Programmable Logic (PL):
  AXI DMA controller
  CNN core
  AXI Stream\Lite interfaces
  Stream – high throughput (input data)
  Lite – static data (kernel/weights)
Design - Top

## Slide 6
Design – CNN Core
  FIFO implementation
    Data is processed “on the fly”
    No PL-PS bottleneck
    AXI Stream for high throughput of processed data
    AXI Lite for configuration / static data
    FPGA resources can be utilized for more CNN layers, or for a bigger sliding window

## Slide 7
  Sliding Window Block
  Convert image section () into vector
  Data reuse – pixel transferred only once
  Block holds pixels, held inside FIFO buffers of size , and registers
  – Image Dimension
  – Kernel Dimension
Design – Sliding Window
Figure: Data reuse / sliding window illustration [source]
Figure: 3x3 neighborhood extractor architecture

## Slide 8
Design – Processing Element
  Single CNN Layer computation
    Convolution
    Pooling (Max/Average)
    Fully Connected
  Stream input/output (AXI Stream)
    Data enters block
    Calculation preformed
    Data streamed deeper into network
  Memory Mapped input (AXI Lite)
    Pass configuration / control data
    Kernels / weights

## Slide 9
Implementation
  Top level data-path
    SW – HW communication
    Input / Output infrastructure
    Will be used as base for CNN data path
Figure: Terminal output. TeraTerm capture
Figure: current project state. Vivado capture

## Slide 10
Simulation
    MNIST
    Keras
  SD card FatFS
  Stats

## Slide 11
Results

## Slide 12
Results

## Slide 13
Conclusion