## Slide 1
מס' פרויקט:
20-1-1-2187
שם הפרויקט: מימוש וסימולציה של מאיץ למערכות לומדות על רכיב FPGA
מגישים: שי צבר 208723627 חיים גרודה 312562721 מנחה:
יוני זייפרט
מקום ביצוע:
אוניברסיטה

## Slide 2
CNN – Convolutional Neural Network
  Achieved great success in image classification, speech recognition and more.
  Research hotspot in many scientific fields.
  Widely used in the industry, such as autonomous robot vision.
  CNN Structure
    Convolution - Feature extraction using filters
    Pooling - Reduce spatial dimensions
    Fully Connected - Final classification decision
Figure: CNN layers [google]
Figure: image recognition illustration [google]

## Slide 3
CNN Acceleration
  Convolutional layers:
    Computationally intensive
    85%-90% of computations [source]
    SW – sequential calculations using nested loops
    HW – parallel calculations
  Pooling
    Reduce spatial dimensions by taking Max/Avg
  Fully Connected
    Matrix multiplications
    Memory Heavy
Figure: 2D convolution. [source]

## Slide 4
System Requirements
  Fixed Point Calculations:
    Better computation time
    Less hardware resources
    Lower accuracy
  High Level Synthesis (HLS)
    RTL abstraction
    Efficiently build and verify hardware
    Better control over optimization of design architecture
  Flexible Implementation:
    Adjustable for different CNN models
    Varying Kernel size, Image size, number of network layers
    Based on FPGA limits
  Simulation:
    Test CNN core operation
    Time comparison with SW
    Accuracy comparison with SW
    SW will run on PS and laptop

## Slide 5
  Processing system (PS):
    CPU – Input, output, control and configuration
    DDR – memory unit
  Programmable Logic (PL):
    AXI DMA controller
    CNN core
  AXI Stream\Lite interfaces
    Stream – high throughput (input data)
    Lite – static data (kernel/weights)
Design - Top

## Slide 6
Design – CNN Core
  FIFO implementation
    Data is processed “on the fly”
    No PL-PS bottleneck
    AXI Stream for high throughput of processed data
    AXI Lite for configuration / static data
    FPGA resources can be utilized for more CNN layers, or for a bigger sliding window

## Slide 7
  Sliding Window Block
  Convert image section () into vector
  Data reuse – pixel transferred only once
  Block holds pixels, held inside FIFO buffers of size , and registers
  – Image Dimension
  – Kernel Dimension
Design – Sliding Window
Figure: Data reuse / sliding window illustration [source]
Figure: 3x3 neighborhood extractor architecture

## Slide 8
Design – Processing Element
  Single CNN Layer computation
    Convolution
    Pooling (Max/Average)
    Fully Connected
  Stream input/output (AXI Stream)
    Data enters block
    Calculation preformed
    Data streamed deeper into network
  Memory Mapped input (AXI Lite)
    Pass configuration / control data
    Kernels / weights

## Slide 9
Current project development status
  Top level data-path
    SW – HW communication
    Input / Output infrastructure
    Will be used as base for CNN data path
Test Block
PS
PL
  Taste of acceleration
    Simple Test Block
    Gain over 10K integer array
    PL uses 25% less clock cycles compared to PS
    That’s with no parallelism yet
Figure: current project state. Vivado capture
Figure: Terminal output. TeraTerm capture

## Slide 10
Updated Timeline
Milestone | Description | Due/completion Date | Notes
CNN Background review | What is CNN? | 01.12.2020 | completed
Learning development tools | Verilog, Vivado, HLS, Zedboard, AXI | 01.12.2020 | completed
Operation Characterization | Complete System design | 15.12.2020 | completed
Top level Data Path infrastructure | implement main data flow interface | 10.01.2020 | completed
Mid-term presentation |  | 18.01.2021 | today
PE block | Implementation and testing | 01.03.2021 | 
Sliding Window block | Implementation and testing | 01.04.2021 | 
CNN integration | Integration of all blocks of the CNN Core and Testing. | 15.04.2021 | 
TOP level integration | Integrating CNN in TOP design | 01.05.2021 | 
Drivers | SW side of CNN | 15.05.2021 | 
Submitting the poster |  | 20.05.2021 | 
Performance improvements | Both HW and SW | 01.06.2021 | 
CNN Simulation |  | 15.06.2021 | 
Project submission |  | 20.06.2021 |