## Slide 1
מס' פרויקט:
20-1-1-2187
שם הפרויקט: מימוש וסימולציה של מאיץ למערכות לומדות על רכיב FPGA
מגישים: שי צבר 208723627 חיים גרודה 312562721 מנחה:
יוני זייפרט
מקום ביצוע:
אוניברסיטה

## Slide 2
CNN – Convolutional Neural Network
  Achieved great success in image classification, speech recognition and more.
  Research hotspot in many scientific fields.
  Widely used in the industry, such as for autonomous cars, security systems, health and more.
  CNN Structure
  Convolution - Feature extraction using filters
  Activation – Introduce nonlinearity
  Pooling - Reduce spatial dimensions
  Fully Connected - Final classification decision
Figure: Implemented CNN model
Video: Tesla computer vision

## Slide 3
Motivation and Objectives
  Motivation
  High accuracy comes with high computation time. Approx. 90% of CNN computations are in the convolutional layers
  Computation resources cause high-power consumption
  Need to include such image recognition capabilities in embedded systems with tight real-time and power constraints
  Objectives
  Acceleration – by hardware parallelization
  Accuracy – reduce loss due to fixed point arithmetic
  Power – dedicated hardware processing elements
Figure: 2D convolution. [source]
Figure: Nested for loop for convolution calculation

## Slide 4
Method
  Fixed Point Calculations:
  Better computation time
  Less hardware resources
  Possible loss of accuracy
  Simulation:
  SW implementation of CNN
  Comparison time HW vs SW
  Compare accuracy HW vs SW
  Evaluate power consumption
  High Level Synthesis (HLS)
  RTL abstraction
  Focus on functionality
  Easily explore algorithmic changes
  Simple platform retargeting
  ZedBoard FPGA
  Programmable logic
  Control design optimization
  Fast development

## Slide 5
  Processing system (PS):
  ARM Cortex A9 667MHz CPU
  Input Output – SD card, UART
  Control and configuration
  DDR memory unit
Hardware Design
  Programmable Logic (PL):
  Artix-7 FPGA with 6.6M logic cells
  DMA controller for data transfer
  Processing Element per CNN layer
  BRAM for kernels and weights
  AXI interfaces
  Stream – high throughput (input data)
  Lite – static data (kernel/weights)

## Slide 6
  Sliding Window
  Neighborhood extraction mechanism
  Memory utilization
  Data reuse – pixel transferred only once
Figures: Data reuse / sliding window illustration
Hardware Design
  Processing Element
  Single CNN layer
  BRAM buffers
  FIFO implementation
Figures: Processing Element design

## Slide 7
Software Design
  Cross platform: PC and FPGA
  Written in C in Vivado SDK
  FPGA platform (ARM Cortex A9 CPU)
  Bare Metal (no OS)
  FatFS – Free file system software module
  Maximum Stack (64Kb)
  PC platform (Intel i7 CPU)
  Linux based
  Single threaded
  Possible Simulation of HW calculations

## Slide 8
HW Implementation
Figure: CNN core block design
Figure: TOP block design
CNN Core
DMA Engine
Processing System
Table: FPGA utilization
Figure: Implemented Design

## Slide 9
Simulation Results
  CNN Simulation
  Python Keras deep learning library
  MNIST dataset, 10K test images
  Kernels and weights fed to CNN
  Measurements
  Avg. image processing time
  Avg. accuracy
  Avg. certainty
  Vivado power estimation
Table: CNN accuracy using different arithmetic
Table: Vivado power estimation results
Table: Time comparison

## Slide 10
Conclusions and Future Work
  Future Work
  Add convolution channels (RGB)
  Compare with multi threaded SW implementations
  Test accuracy loss for different fixed-point schemes
  Conclusions
  Significant acceleration compared to SW
  No loss of accuracy with fixed point
  Significant power conservation

## Slide 11
Appendix and References
  Project repository on GitHub
  ZynqNet - An FPGA-Accelerated Embedded CNN
  Science Direct - Convolutional Neural Networks